## Slide 1: Homework-Ch4

## Slide 2
4-1. A group of N stations share a 56-kbps pure ALOHA channel. Each station outputs a 1000-bit frame on average once every 100 sec, even if the previous one has not yet been sent (e.g., the stations can buffer outgoing frames). What is the maximum value of N?
With pure ALOHA, the usable bandwidth is 0.184×56 kbps = 10.3 kbps. Each station requires 10 bps, so N = 10300/10 = 1030 stations.

## Slide 3
4-2. A large population of ALOHA users manages to generate 50 requests/sec, including both originals and retransmissions. Time is slotted in units of 40 msec.
(a) What is the chance of success on the first attempt?
(b) What is the probability of exactly k collisions and then a success?
(c) What is the expected number of transmission attempts needed?
With 25 slots/second and an average or 50 requests/second, we have G = 2.
Then use the slotted Aloha formulas in Sec. 4.2.1.
(a) With G = 2 Poisson’s Law gives a probability of e-2.
(b) (1 - e-G)k e-G = 0. 135 × 0. 865k.
(c) The expected number of transmissions is eG = 7. 4.

## Slide 4
4-3. What is the length of a contention slot in CSMA/CD for
(a) a 2-km twin-lead cable(signal propagation speed is 82% of the signal propagation speed in vacuum)?, and
(b) a 40-km multimode fiber optic cable (signal propagation speed is 65% of the signal propagation speed in vacuum)?
(a) Signal propagation speed in twin lead is 2. 46 × 108 m/sec. Signal propagation time for 2 km is 8.13 m sec. So, the length of contention slot is 16.26 m sec.
(b) Signal propagation speed in multimode fiber is 1. 95 × 108 m/s. Signal propagation time for 40 km is 205.13 m sec. So, the length of contention slot is 410.26 m sec.

## Slide 5
4-4. Consider five wireless stations, A, B, C, D, and E. Station A can communicate with all other stations. B can communicate with A, C and E. C can communicate with A, B and D. D can communicate with A, C and E. E can communicate A, D and B.
(a) When A is sending to B, what other communications are possible?
(b) When B is sending to A, what other communications are possible?
(c) When B is sending to C, what other communications are possible?
·A
·B
·C
·D
·E
For successful communication we require that the sender can reach (communicate with) the receiver, and that there be no other sender who can reach (now interfere with) the receiver. Also, a station cannot send and receive at the same time.
(a) no other communication is possible.
(b) no other communication is possible.
(c) E can safely send to D since it will not interfere with C’s reception.
Notes: For successful communication we require that the sender can reach (communicate with) the receiver, and that there be no other sender who can reach (now interfere with) the receiver. Also, a station cannot send and receive at the same time.
(a) Since all stations will see A’s packet, it will interfere with receipt of any other packet by any other station. So, no other communication is possible in this case.
(b) B’s packet will be seen by E, A and C, by not by D. Thus, E or C might try to send to D at the same time. However, E and C can communicate with A, so this would interfere with B’s transmission to A. Thus no other communication is possible.
(c) B’s packet will be seen by E, A and C, by not by D. Thus, E or A might try to send to D at the same time. Of these two possibilities, A can communicate with D, so this would interfere with B’s transmission to A. But E can safely send to D since it will not interfere with C’s reception.

## Slide 6
(a) A给B发送数据，BCDE均在A的覆盖范围内。CDE若收数据，则会同时收到A发送的数据，故不可能存在其他通信。
(b) B给A发送数据，ACE在B的覆盖范围。
CE不能作为接收者收数据，否则会同时收到B发送的数据（被干扰）
CE作为发送方给A发送数据，会对B给A发送的数据造成干扰
C作为发送方给D发送数据，C覆盖ABD，会造成A被干扰
E作为发送方给D发送数据，E覆盖ABD，会造成A被干扰
(c) B给C发送数据，ACE在B的覆盖范围。
AE不能作为接收者收数据，否则会同时收到B发送的数据（被干扰）
AE作为发送方给C发送数据，会对B给C发送的数据造成干扰
A作为发送方给D发送数据，然而A覆盖BCDE，会造成C被干扰
E作为发送方给D发送数据，E覆盖ABD，不会干扰C

## Slide 7
4-5. What is the baud rate of classic 10-Mbps Ethernet?
Classic Ethernet uses Manchester encoding, which means it has two signal periods per bit sent. The data rate is 10 Mbps, so the baud rate is twice that, or 20 megabaud.

## Slide 8
4-6. Sketch the Manchester encoding on a classic Ethernet for the bit stream 0001110101.
The signal is a square wave with two values, high (H) and low (L). The pattern is LHLHLHHLHLHLLHHLLHHL.

## Slide 9
4-7. A 1-km-long, 10-Mbps CSMA/CD LAN (not 802.3) has a propagation speed of 200 m/μsec. Repeaters are not allowed in this system. Data frames are 256 bits long, including 32 bits of header, checksum, and other overhead. The first bit slot after a successful transmission is reserved for the receiver to capture the channel in order to send a 32-bit acknowledgement frame. What is the effective data rate, excluding overhead, assuming that there are no collisions?
The round-trip propagation time of the cable is 10 m sec. A complete transmission has six phases:
1. Transmitter seizes cable (10 m sec)
2. Transmit data (25. 6 m sec)
3. Delay for last bit to get to the end (5. 0 m sec)
4. Receiver seizes cable (10 m sec)
5. Acknowledgement sent (3. 2 m sec)
6. Delay for last bit to get to the end (5. 0 m sec)
The sum of these is 58. 8 m sec. In this period, 224 data bits are sent, for a rate of about 3.8 Mbps.

## Slide 10
4-8. An IP packet to be transmitted by Ethernet is 60 bytes long, including all its headers. If LLC is not in use, is padding needed in the Ethernet frame, and if so, how many bytes?
The minimum Ethernet frame is 64 bytes, including both addresses in the Ethernet frame header, the type/length field, and the checksum.
Since the header fields occupy 18 bytes and the packet is 60 bytes, the total frame size is 78 bytes, which exceeds the 64-byte minimum. Therefore, no padding is used.

## Slide 11
4-9. Consider building a CSMA/CD network running at 1 Gbps over a 1-km cable with no repeaters. The signal speed in the cable is 200,000 km/sec. What is the minimum frame size?
For a 1-km cable, the one-way propagation time is 5 µsec, so 2τ=10 µsec. To make CSMA/CD work, it must be impossible to transmit an entire frame in this interval. At 1 Gbps, all frames shorter than 10,000 bits can be completely transmitted in under 10 µsec, so the minimum frame is 10,000 bits or 1250 bytes
L/B >= 2D
L/1Gbps >= 2*1km/200000 km/s
L = 10000 bit

## Slide 12: End