## Slide 1: Switching

## Slide 2: Switching
A
B
C
D
E
F
G
H
(1) circuit switching (in telephone)
(2) packet switching
(3) message switching
Current Internet practice: store-and-forward packet switching
Wide Area Networks:
Dod: ARPANET in 1960s (become Internet)
IBM: SNA in 1974
DEC: DECNET in 1975
CCITT X.25 in 1970s

## Slide 3: Four sources of packet delay
1. Nodal processing
check bit errors
determine output link
A
B
propagation
transmission
nodal
processing
queueing
2. Queueing
time waiting at output link for transmission
depends on congestion level of router

## Slide 4: Delay in packet-switched networks
3. Transmission delay
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
Note: s and R are very different quantities!
A
B
propagation
transmission
nodal
processing
queueing

## Slide 5: Nodal delay
dproc = processing delay
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
  = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs

## Slide 6: Packet switching
- Why not message switching?-
Store-and-Forward
host 1
node 1
node 2
host 2
propagation delay host 1 – node1
processing & set-up delay of a message at node 1
time
message
message
message

## Slide 7: store-and-forward network
A
B
C
A sends a message to C through B.
B must store this message until B is sure that C has received it.
Store first, then forward. But when to start forwarding?
1. After the message is completely received
2. Start forwarding after a fixed amount of information(bits) received
3. Start forwarding immediately after receiving data (cut-through)

## Slide 8: Message switching
EXAMPLE
host 1
node 1
node 2
host 2
for simplicity: ignore processing and propagation delays
M=7.5 Mb
R=1.5 Mbps
transmission delay:
Store complete message and than forward

## Slide 9: Message switching versus packet switching
Example
For simplicity ignore processing and propagation delays
Split the message into packets each with1500 bits long
Store only 1 packet and then forward it
1 ms to transmit packet on 1 link
Pipelining: each link works in parallel
Delay reduced from 15 s to 5.002 s!!!
host 1
node 1
node 2
host 2
R=1.5 Mbps
R=1.5 Mbps
R=1.5 Mbps

## Slide 10: Pipelining
If the message is decomposed into N packets, each packet takes
1/N minutes to travel a link. It takes
minutes.
是分的越细越好吗？
bits
header user information trailer
h
t
overhead for N packets=N(h+t)
overhead for 1 message=h+t

## Slide 11: Packet Switching
each end-end data stream divided into packets
user A, B packets share network resources
each packet uses full link bandwidth
resources used as needed
resource contention:
aggregate resource demand can exceed amount available
congestion: packets queue, wait for link use
store and forward: packets move one hop at a time
  Node receives complete packet before forwarding
Bandwidth division into “pieces”
Dedicated allocation
Resource reservation

## Slide 12: Packet switching versus circuit switching
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability that there are 11 or more simultaneously active users is approximately .0004
Packet switching allows more users to use network!
N users
1 Mbps link

## Slide 13: How do loss and delay occur?
packets queue in router buffers
packet arrival rate to link exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers
Bottleneck in current store-and-forward packet switching network: ROUTING

## Slide 14: Queueing delay
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite!

## Slide 15: Packet loss
queue preceding link in buffer has finite capacity
when packet arrives to full queue, packet is dropped
lost packet may be retransmitted by previous node, by source end system, or not retransmitted at all

## Slide 16: Packet switching versus circuit switching
Advantages of packet switching over circuit switching
  Statistical multiplexing, and therefore efficient bandwidth usage
  Simple to implement
Disadvantages of packet switching over circuit switching
  Excessive congestion: packet delay and high loss
  Protocols needed for reliable data transfer, congestion control
  Packet header overhead
  Provides no transparency to a user
    Analogy: a road versus a railroad

## Slide 17: Packet switching versus circuit switching
Great for bursty data
  resource sharing
  simpler, no call setup
Excessive congestion: packet delay and loss
  protocols needed for reliable data transfer, congestion control
How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem
Is packet switching a “winner?”

## Slide 18: Delay of Circuit Switching and Packet Switching (1)
Compare the delay in sending an x-bit message over a k-hop path in a circuit-switched network and in a (lightly loaded) packet-switched network.
The circuit setup time is s sec, the propagation delay is d sec per hop, the packet size is p bits, and the data rate is b bps.

## Slide 19: Delay of Circuit Switching and Packet Switching (4)
In the above scenario, under what conditions does the packet network have a lower delay?
Under what conditions is a packet-switched network preferable to a circuit-switched?

## Slide 20: Exercise of Circuit Switching and Packet Switching (1)
How long will it take to transmit a 1-GB file from one VSAT to another using a hub as shown in Figure 2-17? Assume that the uplink is 1 Mbps, the downlink is 7 Mbps, and circuit switching is used with 1.2 sec circuit setup time. (the altitude of the satellite is 35,800 km)
Calculate the transmit time in the previous problem if packet switching is used instead. Assume that the packet size is 64 KB, the switching delay in the satellite and hub is 10 microseconds, and the packet header size is 32 bytes.